## Slide 1
My Relief
Don’t let anything stop you!

## Slide 2
Implement a Pain-Relieving Device Using Transcutaneous Electrical Nerve Stimulation “TENS”
Advisor: Dr. Bishoy E. Sedhom Eng. Aya Abdelmonem Eng. Shrouk Mohamed

## Slide 3: Team Members:
Abdallah Abualkhair
Hanan Ahmed
Hussein Ramadan
Israa Elmorsy
Mariam Elhalawany
Mohamed Elaggouri
Reem Elsheikh
Youssef Abo Elyazed
Team Members
Microcontroller Interfacing
Hardware & Testing
PCB Design
Testing
PCB Design
Hardware & Testing
Circuit Analysis
PCB Design
Hardware & Testing
Mobile Application
Microcontroller Interfacing
Testing
Mobile Application
3D Design
Microcontroller Interfacing
Circuit Analysis
Circuit Analysis
Designer
Designer

## Slide 4: Agenda:
Project definition
PCB Design & Circuit
Mobile Application
Results & Future Work
Methodology
3D Design
Microcontroller

## Slide 5: Project Definition

## Slide 6: Problem statement:
Pain is the human’s oldest trouble that has been affecting the human quality of life.
Pain is more than just a feeling of discomfort. It can affect the way you feel overall. It may also lead to mental health conditions, like depression and anxiety.

## Slide 7: TENS
Transcutaneous electrical nerve stimulation (TENS) is a non-invasive peripheral stimulation technique used to relieve pain.
During TENS pulsed electrical currents are delivered across the intact surface of the skin to activate underlying nerves.

## Slide 8: Activity in peripheral nociceptive afferents
releases excitatory neurotransmitters.
causing activity in second order nociceptive transmission cells in the central nervous system.
which leads to pain. Activation of large diameter non-noxious afferents by TENS

## Slide 9: Activity in peripheral nociceptive afferents:
causes the release of inhibitory neurotransmitters which reduce activity in second order nociceptive transmission cells.
The reduction in nociceptive input to the brain results in pain relief.
TENS induced activity in non-noxious transmitting pathways in the central nervous system results in a sensation of electrical paraesthesia.

## Slide 10: Characteristics of different TENS techniques:
Conventional TENS
Acupuncture-like TENS
Intense TENS

## Slide 11: Characteristics of different TENS techniques: 1. Conventional TENS
Physiological Intention
  To selectively activate large diameter non-noxious afferents to elicitsegmental analgesia.
Clinical Technique
  Low-intensity / high-frequency TENS at site of pain to produce “strong but comfortable TENS paraesthesia”. Administer whenever in pain.

## Slide 12: Characteristics of different TENS techniques: 2. Acupuncture-like TENS
Physiological Intention
  To produce muscle twitches to activate small diameter motor afferents to elicit extrasegmental analgesia
Clinical Technique
  High-intensity / low-frequency TENS over muscles, acupuncture points or trigger points to produce “strong but comfortable muscle contractions”. Administer for 15-30 minutes at a time.

## Slide 13: Characteristics of different TENS techniques: 3. Intense TENS
Physiological Intention
  To activate small diameter noxious afferents to elicit peripheral nerve blockade and extrasegmental analgesia.
Clinical Technique
  High-intensity / high-frequency TENS over nerves arising from painful site to produce “maximum tolerable (painful) TENS paraesthesia”. Administer for a few minutes at a time.

## Slide 14: Common conditions for which TENS has been used:
Osteoarthritis
Fibromyalgia
Tendinitis
Bursitis
Diabetic neuropathy
Period Pain

## Slide 15: When to avoid TENS:
Pregnant women: Pregnant women should avoid using TENS in the abdominal and pelvic regions.
People with epilepsy: Applying electrodes to the head or neck of people with epilepsy may induce seizures.
People with heart problems.
People with a pacemaker or another type of electrical or metal implant.

## Slide 16: Goals and objectives:
The goal of this project is to present an easily operated TENS device using a microcontroller to supply electrical impulses. also, the device is controlled by mobile application via Bluetooth to let user choose which program to applied, control the frequency, pulse width value in limit range and set a timer for his therapy session.

## Slide 17: Cost:
1500 EGP
Chart: 
| Electonics copnents | Pads | PCB | 3D | Accessories
Budget | 400 | 400 | 200 | 400 | 150

## Slide 18: Cost:
After studying many products and looking at their prices, we found that most of the prices start from 31 dollars and above, excluding taxes, which is equivalent to 500 Egyptian pounds. These devices are of poor quality as they support some simple programs with a short lifespan.
The price of the device increases with the increase in its quality, as there are devices that exceed 10,000 Egyptian pounds.

## Slide 19: Required:
Mobile application programming.
PCB Design

## Slide 20: Methodology

## Slide 21
Mobile Application
PCB Design
Enclosure 3D Design
Microcontroller Interfacing
Hardware and Testing

## Slide 22: Microcontroller

## Slide 23: Main functions:
Setting TENS values
Communication with Bluetooth.
Battery charge indicator

## Slide 24: Main functions:
Arduino Nano is a microcontroller board designed by Arduino.cc. The microcontroller used in the Arduino Nano is Atmega328, It has a wide range of applications and is a major microcontroller board because of its small size and flexibility.

## Slide 25: Features:
Microcontroller type | ATmega328
Architecture | AVR
Operating voltage | 5 V
Flash memory | 32 KB of which 2 KB used by bootloader
SRAM | 2 KB
Clock speed | 16 MHz
Numbers of IN Analog pins | 8
EEPROM | 1 KB
DC current per I/O pins | 40 mA
Input voltage | 7 – 12 V
Digital I/O pins | 22
PWM output | 6
Power consumption | 19 mA
Size | 18 * 45 mm
Weight | 7 g

## Slide 26: Powering:
The Arduino Nano can be powered via the Mini-B USB connection, 6-20V unregulated external power supply (Vin pin), or 5V regulated external power supply (5V pin).
In our project we depend on last method when we be sure the maximum value it will be 4.2 volt.

## Slide 27: Setting TENS value:
We depend on the Timer1 of Atmega328 microcontroller to produce the resided output we will need for operating tens, which is assigned to pin “D9”.
Timer1 library is a collection of routines for configuring the 16-bit hardware timer called Timer1 on the ATmega168/328.

## Slide 28: Setting TENS value:
PWM (pin, duty, period)
  this will be generating a PWM waveform on the pin9.

## Slide 29: Setting TENS value:

## Slide 31: Communication with HC-05:
Hc-05 Bluetooth module is a special module which can add two-way (full-duplex) wireless functionality to projects.

## Slide 32: Communication with HC-05:

## Slide 33: Battery charge indicator:

## Slide 34: Battery charge indicator:

## Slide 35: PCB & Circuit

## Slide 36: Why PCB design?
Compact Size and Saving of Wire
Ease of Repair and Diagnostic
Saving of Time
Immune to Movement
Low Electronic Noise and Low Cost

## Slide 37: Software designing selected:
Using proteus since it has some features which help us in design:
  Schematic drawing
  Simulation
  Designing PCB
  3D visualization

## Slide 38: Electrical Circuit:
Arduino Nano (ATmega 328)
Transistors (BC327)
Potentiometer
Transformer
Diode
Charge Module
Lithium Battery
Switch
Indicator Led

## Slide 39: Electrical Circuit: 1. Arduino Nano:
The main component that will output a desired signal through timer 1 on pin 9.

## Slide 40: Electrical Circuit: 2. Transistors:
T1(PNP-BC327):
T2(PNP-BC327):
Acts as a safety component for arduino nano
Acts as a switch ON/OFF
T1 will be ON when low voltage is applied on the base terminal
T1 will be ON when low voltage is applied on the base terminal

## Slide 41: Electrical Circuit: 3. Potentiometer:
Which lies between T1 & T2 act as voltage divider and determine the output intensify of T2.

## Slide 42: Electrical Circuit: 4. LED:
Acts as an indicator of the transistor's output and blinks to indicate the frequency and pulse width produced by timer 1.

## Slide 43: Electrical Circuit: 5. Transformer:
Is the final step in the circuit, it function is to step up the voltage from 3v supplied from battery to 25-35v with a load.

## Slide 44: Electrical Circuit: 6. Diode:
When using an inductive load such as transformer, it is advisable to connects a diode directly across the load terminal to absorb any back emf voltage.

## Slide 45: Electrical Circuit: 7. Battery:
Circuit is powered by Li-ion battery 3.7V

## Slide 46: Electrical Circuit: 8. Charge Module:
That used for charging single-cell lithium battery through connecting up to 5V DC supply or a Mini-USB port.

## Slide 47: Final Schematic capture

## Slide 48: PCB

## Slide 49: Final Circuit

## Slide 50: Mobile Application

## Slide 51: Flutter:
Flutter is Google's UI toolkit for building beautiful, natively compiled applications for mobile, web, and desktop from a single codebase. Flutter works with existing code, is used by developers and organizations around the world, and is free and open source.

## Slide 52: Why flutter?
Fast development
Hot reload
Flutter offers a lot of widgets
Expressive and fixable UI
Native performance
Pixel perfect
Uses dart programming language
Cross platform that can be used for android and iOS

## Slide 53: My Relief app:
Homepage
Manual Mode
Body Parts
User
Help video 1
Help video 2
Setting
Precautions
About us

## Slide 54: Home page:
Body Parts
Consists of 11 programs for different parts of human body with pre - programmed parameters , and slider within the safe range for each part.
Manual Mode
Used under doctor supervision , to provide customized programs according to doctor recommendation.

## Slide 55: User page:
Help video 1
how the TENS device used with mobile application .
Help video 2
How to run My Relief

## Slide 56: Setting page:
Precautions
Precautions that must be followed while using the device, such as places where the device is prohibited, such as the face and neck, as well as people prohibited from using the device such as pregnant women, heart patients and epilepsy
About us
Brief about team and project

## Slide 57: Packages and plugins used in flutter app:
Import 'package:flutter_bluetooth_serial/flutter_bluetooth_serial.dart’;
The first goal of this project, started by @edufolly was making an interface for Serial Port Protocol (HC-05 Adapter). Now the plugin features:
Discovering devices (and requesting discoverability),
Listing bonded devices and pairing new ones,
Connecting to multiple devices at the same time,
Sending and receiving data multiple connection
There could be max up to 7 Bluetooth connection
For now, there is only Android support.
Usage :
flutter_bluetooth_serial: ^0.3.0

## Slide 58: Packages and plugins used in flutter app:
import 'package:intl/intl.dart’;
Provides internationalization and localization facilities, including message translation, plurals and genders, date/number formatting and parsing, and bidirectional text.
Usage :
dependencies: intl: ^0.17.0

## Slide 59: Packages and plugins used in flutter app:
import 'package:flutter_app/helper.dart';
A library module containing code that can be shared easily across multiple Flutter or Dart projects.
Usage :
dependencies: helper: ^0.0.14

## Slide 60
Parts Of The Page In Flutter:
App Bar
Body
Navigation Bar

## Slide 61: Navigation Bar:
Bottom Navigation Bar allows you to select one item at a time and quickly navigate to a given page.

## Slide 62
int r= 0;
List<Widget> _widget Options = <Widget>[
Home Page(),
User(),
Setting(),
];
void _on Item Tap(int index) {
set State(() {
r = index;});}
bottom Navigation Bar: Curved Navigation Bar(
color: Color(0xffefd9d9),
background Color: Color(0xffcf6868) ,
height:56,
animation Duration: Duration(milliseconds: 400,),
items: [Icon(Icons.home,size:30,
color: Color(0xff226a7d),),
Icon(Icons.menu_book,size:30,
color: Color(0xff226a7d),),
Icon(Icons.settings_outlined,size:30,
color: Color(0xff226a7d),),],
on Tap: _on ItemTap,),);}

## Slide 63
The body part on the main page of the application:

## Slide 64: Container:
Container class provides a convenient way to create a widget with specific properties: width, height, background color, padding, borders, and more.

## Slide 65
Container(
margin: Edge Insets. only(left: 50, right: 30),
width: 320,
height: 80,
decoration: Box Decoration(
border Radius: Border Radius. circular(80.0),
color: const Color(0xffefd9d9),
border: Border. all(
width: 2, color: const Color(0xff226a7d)),),
alignment: Alignment. center,
child : Material Button(
on Pressed: (){
Navigator . push (
context,
Material Page Route(
builder:(context) => Body Parts(),),);},
child: Text("Body Parts",
style: Text Style(
font Family: 'Script MT',
font Size: 30,
color: const Color(0xff226a7d),
font Weight: FontWeight.w500,),),),),

## Slide 66: Slider:
Slider is a material design widget used for selecting a range of values.

## Slide 67
double frequency = 50;
double pulse = 50;
Slider( value: frequency,
max: 200,
min: 0,
divisions: 40,
active Color: Color(0xffcf6868),
inactive Color: Color(0xff226a7d),
on Change End: (double b) {
set State(() {
frequency = b;
print(frequency);
print('===========================');
_send Text Message To Bluetooth('f' + b.to String());});},
on Changed: (value) { set State(() {
frequency = value;});}),

## Slide 68
Bluetooth
Switch(
active Color: Colors. blue[900],
value: _Bluetooth State.is Enabled,
on Changed: (bool value) {
future() async {
if (value) {
await Flutter Bluetooth Serial.in stance. request Enable();}
else {
await Flutter Bluetooth Serial.in stance. Request Disable();}
await get Paired Devices();
_is Button Unavailable = false;
if (_connected) {
_disconnect();}}
future().then((_) {
set State(() {});});},)

## Slide 69
User:
Open ur1 ()
{
String url1 = "https://www.youtube.com/watch?v=OwEpeJfcMf4";
launch(url1);
}
Open ur2 ()
{
String url1 = "https://www.youtube.com/watch?v=dT2nVlOdNHk";
launch(url1);
}

## Slide 70: 3D Design

## Slide 71: Final Design

## Slide 72
Creating the sketch of the case
Extruding the shape drawn on the sketch

## Slide 73
Applying fillet feature to the edges
Shell feature applied on the solid part

## Slide 74
Creating sketch of the base
Extruding the base with its extensions

## Slide 75
Projecting and extruding bosses and screw holes into the case

## Slide 76
Extruding the electrodes and switch openings into the case
Extruding the micro-USB opening into the case

## Slide 77: Results

## Slide 79
No. | Program | Frequency 'Fr' (Hz) |  | Pulse Width 'PW' (µSec) |  | Period "T" (µSec) |  | Duty (%) |  | Duty in code (0-1023) | 
 |  | Min | Max | Min | Max | Min | Max | Min | Max | Min | Max
1 | Wrist | 50 | 100 | 50 | 60 | 20000 | 10000 | 0.25 | 0.6 | 3.00 | 6.00
2 | Elbow | 1 | 5 | 50 | 300 | 1 000000 | 200000 | 0.005 | 0.15 | 1.00 | 5.00
3 | Shoulder | 4 | 10 | 150 | 250 | 250000 | 100000 | 0.06 | 0.25 | 1.00 | 5.00
4 | Quadriceps | 2 | 150 | 50 | 250 | 500000 | 6667 | 0.01 | 3.75 | 1.00 | 40.00
5 | Mid/Upper back | 2 | 120 | 100 | 250 | 500000 | 8333 | 0.02 | 3 | 1.00 | 35.00
6 | Low Back | 2 | 100 | 75 | 250 | 500000 | 10000 | 0.015 | 2.5 | 1.00 | 30.00
7 | Abdominal cramping | 2 | 30 | 80 | 120 | 500000 | 33333 | 0.016 | 0.36 | 1.00 | 5.00
8 | Hip | 2 | 80 | 100 | 150 | 500000 | 12500 | 0.02 | 1.2 | 1.00 | 15.00
9 | Knee | 5 | 150 | 50 | 150 | 200000 | 6667 | 0.025 | 2.25 | 1.00 | 25.00
10 | Ankle | 5 | 150 | 50 | 200 | 200000 | 6667 | 0.025 | 3 | 1.00 | 30.00
11 | Hand / Foot | 2 | 150 | 150 | 220 | 500000 | 6667 | 0.03 | 3.3 | 1.00 | 35.00

## Slide 80: In this example we set in code the 40 Hz frequency value and 30 Duty cycle whish is equal a 3% as an actual duty cycle.

## Slide 81: Measure the value of battery volt.

## Slide 84: Side effect:
Tens units is safe for most people and will not usually experience any side effects.
the electrical impulses that a TENS unit produces may cause a buzzing, tingling, prickling sensation. or people may be allergic to the adhesive pads.

## Slide 85: Future Work

## Slide 86: Future Work:
Smaller
(Using nanotechnology)
More Efficiently
Less session Time
Built in with Electrodes

## Slide 87: Future Design:

## Slide 88: Future Design:

## Slide 89: Thanks
All copyrights reserved for My Relief Team.